## Slide 1: Lean Six Sigma Project on Reducing Defects in Ampoules at Mercury Laboratories Ltd.
Guided by- Prof. K. MURALIDHARAN
Miss AKRUTI SHUKLA
Presented by:
Ira Chakraborty
Vernal Damor
Brijesh Dubey
Kunj Panchal

## Slide 2: Company Profile
Founded in 1962, with the vision to be a leading manufacturer of pharmaceutical products with
  Highest ethical standard.
  Generate long lasting customer loyalty.
  Providing outstanding quality , service and customer satisfaction.
The company began producing pharmaceutical products for mother and child healthcare and subsequently introduced products in all dosage forms like tablets, capsules, liquids and injectable.
They have their reputed presence in more than 20 countries directly and in more than 15 countries indirectly, they are present in Asia, Africa and Far East countries and they will be in USA and European Countries in few years.

## Slide 3: Overview of the Ampoules manufacturing process
Importing
They are imported.
Random Sampling done.
Washing
The number of Ampoules/Vials are pre-decided a day before based on solution required.
Two machines : 1) Only Ampoules 2) Both Ampoules and Vials.
DHS
Dry Heating Sterilization.
Chances of defects.
Approval by Packaging Dept. for use.
Filling
Arranged in trays after washing and sent to DHS.
Visual Inspection
Solution is filled in Ampoules/Vials.
They are sealed here.
Defects possible.
Sealed Ampoules/Vials are checked for :Black Particles, Glass, Empty or broken products
More chances of defects (5%).
Dispatch
After visual inspection, they are labelled and packed, ready for dispatch.
Labelling contains error.
0.1% breakage failure in dispatch.

## Slide 4
Project Roadmap

## Slide 5: Define Phase Roadmap
DEFINE
PROJECT CHARTER
SIPOC
MEASURE
GANTT CHART
ANALYSE
IMPROVE
CONTROL

## Slide 6
Customer: - External: Whole Sale Customers. Internal: Quality Assurance and Inspection | Timeline: See Gantt Chart Define Measure Analyze Improve Control
Problem Statement: Low Sigma Level High Transit Time | Objective Statement: Improving Quality of entire process: In terms of cost. In terms of time. In terms of Sigma level.
Primary Concern: Reducing defects in ampoules. Improving sigma level of the process Decreasing Transit Time | Guide: Dr. Prof. K. Muralidharan Ms. Shukla Akruti Team Members: Kunj Panchal Brijesh Dubey Ira Chakraborty Vernal Damor
PROJECT CHARTER
Title: “Lean Six Sigma Project on Reducing Defects in Ampoules at Mercury Laboratories Ltd.”

## Slide 7: SIPOC
 | S | I | P | O | C
Process | Supplier | Input | Critical Process Steps | Output | Customer
Washing | F-Scout (Ampoule bottle manufacturing Company) | Ampoules | Loading Washing Placing in trays | Washed Ampoules | Filling Process
Filling | Washing | Washed Ampoules Solution | Loading Filling Unloading | Filled Ampoules | Cleaning
Cleaning | Filling Process | Filled Ampoules | Water Testing Cleaning of Sticky Solution Drying of Ampoules | Cleaned Ampoules | Visual Testing
Visual Testing | Cleaning | Cleaned Ampoules | Glass Testing Fiber Testing Particle Testing | Tested Ampoules | Packaging
Packaging | Tested Ampoules | Tested Ampoules | Box Making Labelling Box Filling | Packaged Ampoules | Production Unit

## Slide 8: Gantt Chart
Company Name: Mercury Laboratories Limited |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Month | December |  | January |  |  |  | February |  |  |  | March |  |  |  | April | 
 | Week | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2
Define | Scheduled |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Actual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Measure | Scheduled |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Actual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Analysis | Scheduled |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Actual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Improvement | Scheduled |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Actual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Control | Scheduled |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Actual |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
The Gantt chart is a simple horizontal Bar chart, where bars represents the actual calendar time which is planned for each task. The scale used for this will depend on the overall size of the project.

## Slide 9: Define Phase Summary:
We started by preparing the Project Charter. Gantt chart which represents the actual calendar time which is planned for each phase of DMAIC. Then we used SIPOC for better understanding of the process .

## Slide 10: Measure Stage Roadmap
DEFINE
MEASURE
ANALYSE
IMPROVE
CONTROL
Data Collection
Process Sigma Level

## Slide 11: DATA COLLECTION SHEET
Our main purpose to collect the data was to find out the defects in each process of ampoules starting from washing upto packaging.
We started collecting our data from 22nd December 2016.

## Slide 12: Initial Process Sigma Level

## Slide 13: ANALYSIS PHASE ROADMAP
DEFINE
MEASURE
ANALYSE
IMPROVE
CONTROL
FMEA
Cause and Effect Diagram
Pareto chart
5S Methodology

## Slide 14: Cause and Effect Diagram

## Slide 15: Causes of Defects in each process:
1. Washing Process
Cause of defects |  | Machine 1 | Machine 2
1.While loading: | Setting the ampoules wrongly in the washing needles. | 50% | 40%
2.While Washing | Due to manual pressure exerted on the lid over misplaced ampoules. | 0% | 37%
3.While placing Ampoules in tray: | Mishandling of the washed ampoules while placing on tray. | 50% | 23%
Chart: Pie chart for defects in Machine 1
| While Loading | while washing | while placing in trays
 | 12 | 0 | 12
Chart: Pie chart for defects in Machine 2
| While Loading | while washing | while placing in trays
Machine 2 | 39 | 37 | 23

## Slide 16
2. Cleaning Process
Causes of Defects |  | %
Defects while performing water test: | Breakage during dry heat sterilization can be indicated when the water test is being performed. | 63
Other reasons | Drying the wet ampoules after water test is done manually, which leads to breakage. | 37
Chart: Breakage during cleaning process
| Throwing in plastic container | Other reasons
Total defects | 77 | 45

## Slide 17
3. Visual Inspection Process
The ampoules are checked for the following defects:
  Black particle
  White particle
  Glass particle
  Fiber
  Volume
  Sealing
  Breakage
They are considering Black & White Fiber particles as one defect namely Fiber.
They are considering Sealing and Breakage as Breakage Defect

## Slide 18
Causes of defects (Visual Inspection) |  | %
Breakage | The breakage in the ampoules can be found due to mishandling in the drying process or due to mishandling while carrying it to the visual testing unit. | 50
Glass | Glass may get inside the ampoules in the sealing process. | 32
Fibers | Dry heat sterilization process may leave black or while fibers inside the ampoules which may be detected in visual testing process. | 18
Chart: Pie chart showing defects in the process of Visual Inspection
| Breakage | Glass | Fibres
 | 14 | 9 | 5

## Slide 19
4. Packaging Process
Reasons | Causes | %
GSM of labels more than required. | Required GSM of label is 70-75 but it comes in range of 90-95 from the labeling company. | 30%
Wrong side printing on label. | Due to printing of label on the wrong side of bind of the paper, the label gets less removed. | 
Solution on outside | The solution is still present on the outside of ampoules even after the process of cleaning them. | 
Breakage | The ampoules still gets broken at this stage due to wear and tear of all the processes. | 70%
Chart: Pie Chart for defects in Packaging process
| Labelling Problem | Breakage
 | 16 | 37

## Slide 20: FMEA (Failure Mode Effect Analysis)
Failure modes and effects analysis (FMEA) is a set of guidelines, a process, and a form of identifying and prioritizing potential failures and problems in order to facilitate process improvement.
Severity: Assesses the seriousness of the effect of the potential failure mode to the next component if it occur. Estimation is typically based on a 1–10 scale where 10 is the most serious, 5 is low, and 0 is no effect.
Occurrence: Estimates the likelihood that a specific cause will occur. Estimation is usually based on a 1–10 scale where 10 is very high, 5 is low, and 1 is remote.
Detection: Assessment of the ability of the current design control to detect the subsequent failure mode. Assessment is based on a 1–10 scale where 10 is absolute uncertainty, 5 is moderate, 1 is almost certain.
Risk priority number (RPN): Product of severity, occurrence, and detection rankings. The ranking of RPN prioritizes design concerns.

## Slide 21: FMEA FOR WASHING
Interpretation: We can observe from above table that RPN is highest for breakage of ampoules in machine 2. Hence it should be revised and try to reduce it.

## Slide 22
Potential failure Mode | Recommendations | Reason
Loading M1 | Not too fast assembling (time taken should be more than 5 mins) | From the Pie chart for M1 given below we see that if the time taken to load the machine is greater than 5 mins, it amounts to less number of defectives .
Loading M2 | Not too fast assembling (time taken should be more than 11 mins) | From the Pie chart for M2 given below we see that if the time taken to load the machine is greater than 12 mins, it amounts to less number of defectives .
Washing | Not to wash in Ampoules in M2 | 
Chart: Machine 1
| <5minutes | >5minutes
Breakage | 15 | 9
Chart: Machine 2
| <11minutes | >11minutes
Breakage | 56 | 43

## Slide 23: Chi Square Test For Association (M1)
H0: | There is no association between defectives and time <5 minutes |  |  |  |  |  |  |  |  | 
H1: | There is association between defectives and time <5 minutes |  |  |  |  |  |  |  |  | 
time taken | Breakage | non defective | Total | Chi-Sq | 3 |  | Breakage Expected | non defective Expected |  | 
<5minutes | 15 | 9 | 24 | p | 0.083265 |  | 12 | 12 |  | 
>5minutes | 9 | 15 | 24 | a | 0.05 |  | 12 | 12 |  | 
Total | 24 | 24 | 48 | Variables are Independent |  |  |  |  |  | 
 | Breakage | non defective | Contribution |  |  |  |  |  |  | 
<5minutes | 0.75 | 0.75 |  |  |  |  |  |  |  | 
>5minutes | 0.75 | 0.75 |  |  |  |  |  |  |  | 
CONCLUSION: | Here as p value > 0.05 hence, we do not reject our null hypothesis |  |  |  |  |  |  |  |  | 
 | therefore we can say that there is no association between defectives and time < 5minutes |  |  |  |  |  |  |  |  | 

## Slide 24: Chi Square Test For Association (M2)
H0: | There is no association between defectives and time <11 minutes |  |  |  |  |  |  |  |  | 
H1: | There is association between defectives and time <11minutes |  |  |  |  |  |  |  |  | 
time taken | Breakage | non defective | Total | Chi-Sq | 45.09090909 |  | Breakage Expected | non defective Expected |  | 
<11minutes | 56 | 43 | 99 | p | 0.00000000016167 |  | 66 | 33 |  | 
>11minutes | 43 | 56 | 99 | a | 0.05 |  | 66 | 33 |  | 
 | 99 |  | 99 | Variables are Related |  |  | 66 | 33 |  | 
Total | 198 | 99 | 297 |  |  |  |  |  |  | 
 | Breakage | non defective | Contribution |  |  |  |  |  |  | 
<11minutes | 1.515152 | 3.03030303 |  |  |  |  |  |  |  | 
>11minutes | 8.015152 | 16.03030303 |  |  |  |  |  |  |  | 
0 | 16.5 | 33 |  |  |  |  |  |  |  | 
CONCLUSION: | Here as p value < 0.05 hence,we reject our null hypothesis |  |  |  |  |  |  |  |  | 
 | therefore we can say that there is association between defectives and time < 11minutes |  |  |  |  |  |  |  |  | 

## Slide 25: FMEA FOR VISUAL INSPECTION
Interpretation: We can observe from above table that RPN is highest for rejection of ampoules due to defects within ampoules. Hence it should be revised and reduced.

## Slide 26
Potential failure Mode | Recommendations | Reason
Cleaning after DHS | Use Thermocol Cartons | From the Pie chart given below we see that the breakage due to Throwing the ampoules in plastic containers amounts to more percentage of defectives while cleaning Ampoules than that of other reasons.
Defects within Ampoules | Maintenance of DHS machine | Defects within ampoules, presence of glass and fibers can be reduced only by maintenance of the DHS machine.

## Slide 27: Chi Square Test For Association (Cleaning)
H0: | There is no association between defectives and throwing in plastic container |  |  |  |  |  |  |  |  | 
H1: | There is association between defectives and throwing in plastic container |  |  |  |  |  |  |  |  | 
Breakage | Total defects | nondefective | Total | Chi-Sq | 69.71857923 |  | Total defects Expected | nondefective Expected |  | 
Throwing in plastic container | 77 | 45 | 122 | p | 0.0000000000000007258 |  | 81.33333 | 40.66667 |  | 
Other reasons | 45 | 77 | 122 | a | 0.05 |  | 81.33333 | 40.66667 |  | 
 | 122 |  | 122 | Variables are Related |  |  | 81.33333 | 40.66667 |  | 
Total | 244 | 122 | 366 |  |  |  |  |  |  | 
 | Total defects | nondefective | Contribution |  |  |  |  |  |  | 
Throwing in plastic container | 0.230874 | 0.461749 |  |  |  |  |  |  |  | 
Other reasons | 16.23087 | 32.46175 |  |  |  |  |  |  |  | 
0 | 20.33333 | 40.66667 |  |  |  |  |  |  |  | 
CONCLUSION: | Here as p value < 0.05 hence,we reject our null hypothesis |  |  |  |  |  |  |  |  | 
 | therefore we can say that there is association between defectives and throwing in plastic container |  |  |  |  |  |  |  |  | 

## Slide 28: FMEA for PACKAGING
Interpretation: We can observe from above table that RPN is highest for wrong side printing and solution left on ampoules during labelling. Hence it should be revised and reduced.

## Slide 29
Potential failure Mode | Recommendations | Reason
Wrong GSM | Contact Label company to correct it | Since labels are not manufactured in Mercury Laboratories
Wrong side printing | Contact Label company to correct it | Since labels are not manufactured in Mercury Laboratories
Solution on Amp. | More effective cleaning required (Use of lukewarm water) | Cost effective solution to this problem
Breakage of Amp. | Strict surveillance | The pie Chart below shows the percentage of breakage under surveillance is more than when the process is not under surveillance.

## Slide 30: Chi Square Test For Association For Packaging
H0: | There is no association between defectives and under survalliance |  |  |  |  |  |  |  |  | 
H1: | There is association between defectives and under survalliance |  |  |  |  |  |  |  |  | 
Breakage | Total defects | non defective | Total | Chi-Sq | 12.16216 |  | Total defects Expected | non defective Expected |  | 
Under survalliance | 11 | 26 | 37 | p | 0.000488 |  | 18.5 | 18.5 |  | 
Not under survalliance | 26 | 11 | 37 | a | 0.05 |  | 18.5 | 18.5 |  | 
Total | 37 | 37 | 74 | Variables are Related |  |  |  |  |  | 
 | Total defects | non defective | Contribution |  |  |  |  |  |  | 
Under survalliance | 3.040540541 | 3.040541 |  |  |  |  |  |  |  | 
Not under survalliance | 3.040540541 | 3.040541 |  |  |  |  |  |  |  | 
CONCLUSION: | Here as p value < 0.05 hence,we reject our null hypothesis |  |  |  |  |  |  |  |  | 
 | therefore we can say that there is association between defectives and under survalliance |  |  |  |  |  |  |  |  | 

## Slide 31: Pareto Chart
Process | Total defects(out of 10000)
Washing (Machine 1) | 19
Washing (Machine 2) | 138
Cleaning | 244
Visual Testing | 1900
Packaging | 53
Interpretation:
From this chart we can see that the Bar chart is the frequency of defects in descending order. Whereas the line chart is the % cumulative frequency of the defects in ascending order. We can observe that the maximum defect comes from Visual Inspection.

## Slide 32: 5S Methodology
SEIRI (Structurize)
The washing room is not well structured. The time taken to set ampoules in Machine 2 is 7 mins (on an average) more
than that of Machine 1.
The belt used in the process of packaging is old and worn out (been in use for more than 29 years).
SEITON (Systemize)
The ampoules in Machine 1 are not set systematically (upside down) leading to loss of 2 mins (on an average) on every set of 500 Ampoules.
The process of cleaning and drying is done manually this leads to breakage of Ampoules. A systematic procedure might reduce the number of breakage.
SEISO (Sanitize)
The water in cleaning process should be changed after 24 batches i.e. 2 hours.
The room for washing should be swept every 2 hours to avoid wet floors.
SEITKESU (Standardize)
Standardize procedure should be used for cleaning procedure.
SHITSUKE (Self-discipline)
The recess hours are 12 to 12:30 and 2:30 to 2:40, we observed that the workers their work 5 – 10 minutes late. Hence self-discipline should be enforced.

## Slide 33: Improvement Phase Roadmap
DEFINE
MEASURE
ANALYSE
IMPROVE
CONTROL
Process Sigma Level
Improvements

## Slide 34: Final Sigma Level
In Washing process, Ampoules were placed slowly and the no. of defects were noted.
In Packaging process, the labeling process was done under surveillance and the defects were noted.
In Visual Inspection, the improvements were not possible from our end.
Thus it can be seen that the sigma levels have increased in both the processes.
Washing – Machine 1 = Increment of 0.17
Washing – Machine 2 = Increment of 0.24
Packaging = Increment of 0.21

## Slide 35
Cleaning process
Total no. of Units checked | 5000
No. of defects | 64
DPU | 0.0128
DPMO | 6400
Sigma level (long term) | 2.49
Sigma level (short term) | 3.99

## Slide 36: Sigma Level
Process | Sigma level (Before) | Sigma Level (After)
Washing (M1) | 3.22 | 3.39
Washing (M2) | 2.61 | 2.85
Cleaning | 2.25 | 2.49
Packaging | 2.79 | 3.00

## Slide 37: Control Phase Roadmap
DEFINE
MEASURE
ANALYSE
IMPROVE
CONTROL
Control Charts
Suggestions

## Slide 38: Control Chart
np CHART
the np-chart is a type of control chart used to monitor the number of nonconforming units in a sample.
This assumption is the basis for the calculating the upper and lower control limits. The control limits are calculated as:
LCL = np –3 np (1 – p)
UCL= np + 3 np(1 – p)
where n is the number of items and p is the proportion of defective items. Also, zero serves as a lower bound on the LCL value.

## Slide 39
Chart: Total Defects np Chart of Washing process (Machine 1)
| Batch 1 | Batch 2 | Batch 3 | Batch 4 | Batch 5 | Batch 6 | Batch 7 | Batch 8 | Batch 9 | Batch 10 | Batch 11 | Batch 12 | Batch 13 | Batch 14 | Batch 15 | Batch 16 | Batch 17 | Batch 18 | Batch 19 | Batch 20 | Batch 21 | Batch 22 | Batch 23 | Batch 24 | Batch 25
Total Defects | 0 | 0 | 0 | 1 | 2 | 3 | 1 | 0 | 0 | 0 | 0 | 4 | 3 | 0 | 0 | 0 | 1 | 2 | 2 | 2 | 0 | 0 | 0 | 1 | 2
UCL | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966 | 3.8966
+2 Sigma | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177 | 2.9177
+1 Sigma | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389 | 1.9389
Average | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96
-1 Sigma | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
-2 Sigma | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
LCL | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Interpretation: The process is going out of Control Limits

## Slide 40
Chart: Total Defects np Chart of Washing process (Machine 2)
| Batch 1 | Batch 2 | Batch 3 | Batch 4 | Batch 5 | Batch 6 | Batch 7 | Batch 8 | Batch 9 | Batch 10 | Batch 11 | Batch 12 | Batch 13 | Batch 14 | Batch 15 | Batch 16 | Batch 17 | Batch 18 | Batch 19 | Batch 20 | Batch 21 | Batch 22 | Batch 23 | Batch 24 | Batch 25
Data1 | 18 | 4 | 4 | 2 | 5 | 3 | 1 | 2 | 1 | 1 | 5 | 2 | 3 | 4 | 2 | 5 | 4 | 2 | 7 | 1 | 6 | 5 | 6 | 2 | 4
UCL | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887 | 9.8887
+2 Sigma | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125 | 7.9125
+1 Sigma | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362 | 5.9362
Average | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96 | 3.96
-1 Sigma | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838 | 1.9838
-2 Sigma | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071 | 0.0075071
LCL | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Interpretation: The process is going out of Control Limits

## Slide 41
Chart: Total Defects np Chart for Cleaning Process
| Batch 1 | Batch 2 | Batch 3 | Batch 4 | Batch 5 | Batch 6 | Batch 7 | Batch 8 | Batch 9 | Batch 10 | Batch 11 | Batch 12 | Batch 13 | Batch 14 | Batch 15 | Batch 16 | Batch 17 | Batch 18 | Batch 19 | Batch 20 | Batch 21 | Batch 22 | Batch 23 | Batch 24 | Batch 25
Data1 | 15 | 8 | 2 | 3 | 5 | 9 | 9 | 2 | 3 | 6 | 0 | 3 | 0 | 10 | 5 | 4 | 3 | 4 | 4 | 2 | 3 | 6 | 4 | 3 | 9
UCL | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259 | 11.4259
+2 Sigma | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439 | 9.2439
+1 Sigma | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062 | 7.062
Average | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88 | 4.88
-1 Sigma | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698 | 2.698
-2 Sigma | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609 | 0.51609
LCL | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Interpretation: The process is going out of Control Limits

## Slide 42
Chart: Total Defects np Chart for Visual Inspection process
| Batch 1 | Batch 2 | Batch 3 | Batch 4 | Batch 5 | Batch 6 | Batch 7 | Batch 8 | Batch 9 | Batch 10 | Batch 11 | Batch 12 | Batch 13 | Batch 14 | Batch 15 | Batch 16 | Batch 17 | Batch 18 | Batch 19 | Batch 20 | Batch 21 | Batch 22 | Batch 23 | Batch 24 | Batch 25
Data1 | 2 | 1 | 2 | 3 | 1 | 2 | 1 | 1 | 2 | 1 | 2 | 5 | 2 | 0 | 1 | 2 | 0 | 2 | 0 | 1 | 1 | 2 | 1 | 1 | 2
UCL | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488 | 4.8488
+2 Sigma | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392 | 3.7392
+1 Sigma | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296 | 2.6296
Average | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52 | 1.52
-1 Sigma | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041 | 0.41041
-2 Sigma | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
LCL | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Interpretation: The process is going out of Control Limits

## Slide 43
After improvements:
Chart: Total Defects np Chart of Washing process (Machine 1)
| Batch 1 | Batch 2 | Batch 3 | Batch 4 | Batch 5 | Batch 6 | Batch 7 | Batch 8 | Batch 9 | Batch 10 | Batch 11 | Batch 12 | Batch 13 | Batch 14 | Batch 15 | Batch 16 | Batch 17 | Batch 18 | Batch 19 | Batch 20 | Batch 21 | Batch 22 | Batch 23 | Batch 24 | Batch 25
Total Defects(M1) | 1 | 0 | 0 | 1 | 1 | 2 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 2 | 1 | 1 | 0 | 0 | 1 | 0
UCL | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607 | 2.6607
+2 Sigma | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471 | 1.9471
+1 Sigma | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336 | 1.2336
Average | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52 | 0.52
-1 Sigma | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
-2 Sigma | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
LCL | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Interpretation: The process is in Control Limits after the improvements.

## Slide 44
After improvements:
Chart: Total Defects np Chart of Washing process (Machine 2)
| Batch 1 | Batch 2 | Batch 3 | Batch 4 | Batch 5 | Batch 6 | Batch 7 | Batch 8 | Batch 9 | Batch 10 | Batch 11 | Batch 12 | Batch 13 | Batch 14 | Batch 15 | Batch 16 | Batch 17 | Batch 18 | Batch 19 | Batch 20 | Batch 21 | Batch 22 | Batch 23 | Batch 24 | Batch 25
Total Defects(M2) | 1 | 1 | 2 | 2 | 3 | 1 | 0 | 2 | 1 | 2 | 3 | 2 | 1 | 2 | 2 | 2 | 3 | 2 | 2 | 2 | 2 | 3 | 2 | 2 | 2
UCL | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357 | 5.8357
+2 Sigma | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171 | 4.5171
+1 Sigma | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986 | 3.1986
Average | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88 | 1.88
-1 Sigma | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143 | 0.56143
-2 Sigma | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
LCL | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Interpretation: The process is in Control Limits after the improvements.

## Slide 45
Chart: np Chart for cleaning (Improved)
| Batch 1 | Batch 2 | Batch 3 | Batch 4 | Batch 5 | Batch 6 | Batch 7 | Batch 8 | Batch 9 | Batch 10 | Batch 11 | Batch 12 | Batch 13 | Batch 14 | Batch 15 | Batch 16 | Batch 17 | Batch 18 | Batch 19 | Batch 20 | Batch 21 | Batch 22 | Batch 23 | Batch 24 | Batch 25
Data1 | 2 | 5 | 2 | 1 | 4 | 4 | 2 | 2 | 3 | 4 | 2 | 3 | 1 | 2 | 3 | 1 | 3 | 2 | 2 | 1 | 3 | 3 | 3 | 3 | 3
UCL | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076 | 7.1076
+2 Sigma | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917 | 5.5917
+1 Sigma | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759 | 4.0759
Average | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56 | 2.56
-1 Sigma | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441 | 1.0441
-2 Sigma | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
LCL | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
After improvements:
Interpretation: The process is in Control Limits after the improvements.

## Slide 46: Suggestions
In the Washing process, the Machine for vials should not be used to wash Ampoules, if possible.
New machinery should be brought, in order to reduce defects in Visual Inspection process.
In Cleaning process, there should be a change in the method where the Ampoules are cleaned manually.
For Packaging process, the label company should be contacted and the problems should be mentioned to them. Further the conveyer belt in the labeling process should be replaced. If possible, the automatic Labeling machine should be taken into use.

## Slide 47: References
Six Sigma for Organizational Excellence - A Statistical Approach,
Prof. K. Muralidharan
2. Minitab 17 – Statistical Software
Quality Companion 3
www.iSixSigma.com

## Slide 48: Thank you